Las Flores Non-Profit Housing Corporation

Bid Documents for

Painting of

Underground Garage

at  10 Dora Avenue, Toronto, Ontario

September 13, 2010

Las Flores Non-Profit Housing Corporation

c/o Community First Developments Inc.

10 Dora Avenue

Toronto, Ontario M6H 2J4

Telephone: 416-588-1252

Fax: 416-588-7992

1	General instructions

1.1	Las Flores Non-Profit Housing Corp. (the "Non-Profit") located at 10 Dora Avenue, Toronto, Ontario is asking for Bids from experienced companies to provide re-painting to the ceiling and wall surfaces, pipes and service doors, parking lines numbers and signs at the underground parking level.

1.2	Your bid should include all permit costs, if any, to complete this project.

Quality Control

1.3	The Contractor shall be experienced in painting undergound garage.

Material Delivery, Storage & Handling

1.4	Deliver paint/materials to job-site in new, dry, unopened, and well-marked containers showing product and manufacturer's name.  Deliver materials in sufficient quantity to allow continuity of work.

1.5	Store paint/materials in dry area protected from weather condition.  Storage of materials inside the facility and/or at areas of the grounds is permitted only where designated and only with consent from the Management of Las Flores Non-Profit Housing Corp.

Site Condition

1.6	Contractor shall be responsible to police his men to ensure all areas where his men are working is kept clean, neat, and orderly.  At conclusion of job, an inspection will be done to satisfy the Management all areas of the building and grounds are in their original condition.

Safety Requirements

1.7	All application, material handling, and associated equipment shall conform to and be operated in conformance with WSIB and WHMIS safety requirements.  The Contractor shall have all applicable Material Data Safety Sheets on site and available for review at all times.  The Contractor must comply with City of Toronto fire and safety requirements.  The Contractor must notify the Management whenever work is expected to be hazardous to the building residents and/or employees.

Warranty

1.8	The Contractor shall provide a 2-year labor and material warranty.

Lump-sum Prices

1.9	The Contractor shall provide lump-sum prices for the following items:

a.	All wall, column and ceiling surfaces		$__________

b.	All mechanical pipes				$__________

c.	All service door surfaces & frames		$__________

d.	All parking lines, numbers & signs		$__________

Important Dates

1.10	a.	Deadline for bid submission:		Wednesday, Sept. 22, 2010 at 3:00 p.m.

b.	Project commitment:			late September, 2010

c.	Project commencement (estimated)	October, 2010

d.	Project completion (estimated)	November, 2010

Note:	A project schedule shall be prepared and mutually agreed by the Contractor and the Management.  Such schedule is to cause the least disturbance to the building residents and must be strictly followed by the Contractor.

2	Scope of work

Materials

2.1	The materials to be used are:

a.	Walls, columns & ceiling – Benjamin Moore Super Spec Interior latex, semi-gloss finish, K276, white color (paint color code to be confirmed)

b.	Lower portion (36 inches from floor surface) of walls and columns – Benjamin Moore Super Spec Interior latex, semi-gloss finish, K276, grey color to comply with building code (paint color code to be confirmed)

c.	Mechanical pipes & ventilation cages – Benjamin Moore Collection Exterior Alkyd High-Gloss Enamel, 133, with color to comply building and/or safety code

d.	Service doors & frames – Benjamin Moore Collection Exterior Alkyd High-Gloss Enamel, 133, color to be determined

e.	Parking lines – Benjamin Moore, MooreSpec Industrial Coatings M58, Safety & Zone marking latex, yellow traffic paint (M58-10)

f.	Parking space numbers and signs – Benjamin Moore, MooreSpec Industrial Coatings M58, Safety & Zone marking latex, color to comply with building code and/or City by-laws

Application Instructions

  - All paints are to be applied as per paint manufacturer’s technical data sheets.

  - Wall, column & ceiling surfaces:

- As paint is to be applied by spray, preparattion must include covering all surfaces that are not to be spray-painted, i.e. pipes, sprinklers heads, floors, etc.  While the residents are expected to remove their vehicles from the garage, the random vehicles left must be covered up as well.  Extra attention must be given to ensure all sprinkler heads are 100% covered only during the spray process.

- Clean surfaces to be painted with manual tools and/or power blower.

- Apply paint with commercial sprayer to all surfaces (except the surfaces to be painted in grey color.

  - Lower portion of wall & column surfaces:

- As paint is to be applied by spray, preparattion must include covering all surfaces that are not to be spray-painted, i.e. pipes, sprinklers heads, floors, etc.  While the residents are expected to remove their vehicles from the garage, the random vehicles left must be covered up as well.  Extra attention must be given to ensure all sprinkler heads are 100% covered only during the spray process.

- Clean surfaces to be painted with manual tools and/or power blower.

- Apply grey paint with commercial sprayer to all surfaces.

  - Mechanical pipes & ventilation cages:

- Thoroughly clean surfaces to be painted with manual tools.  If the surface appears to be rusty, rust must be removed with steel brush (manual or power).

- Apply one coat of Tremclad rust, color to comply with building/safety code.

  - Service doors & frames:

- Thoroughly clean surfaces to be painted.

- Apply one coat of Benjamin Moore alkyd paint, color to be determined.

  - Parking lines:

- Thoroughly clean surfaces to be painted.

- Apply Benjamin Moore yellow traffic paint on all existing parking lines.

  - Parking space numbers & signs:

- Thoroughly clean surfaces to be painted.

- Apply paint using acceptable stencils.

BID FORM

To:	Las Flores Non-Profit Housing Corporation

From:		Name and address of Bidder:

Job Site:	10 Dora Avenue, Toronto

The undersigned Bidder, having carefully examined the Bidding and Contract Requirements, Conditions of the Contract, Drawings, Specifications, dated September 13, 2010, and all subsequent Addenda, all as issued by the Owner, having visited the site, and being familiar with all conditions and requirements of the Work, hereby agrees to furnish all material, labor, equipment and services as described in the above documents, without exception, to complete:

The Contract for the above-named Project, in accordance with the requirements of the Bidding Documents, for the sum of:

Lump-sum Prices:

- All wall, column and ceiling surfaces		$__________

- All mechanical pipes				$__________

- All service door surfaces & frames		$__________

- All parking lines, numbers & signs		$__________

TOTAL	$__________

HST extra

Time of Completion

The undersigned Bidder proposes and agrees hereby to commence the Work of the Contract Documents on a date specified in a written Notice to Proceed to be issued by the Owner and shall fully complete the Work within the Contract Time indicated in the Supplementary Conditions.

Acknowledgement of Addenda

The undersigned Bidder acknowledges receipt of and use of the following Addenda in the preparation of this Bid:

Addendum No. 1, dated _____________

The undersigned further states that he/she is a duly licensed Contractor in the Province of Ontario, and that all fees, permits, insurance, WSIB, etc., pursuant to the submission of this proposal have been paid in full.

SIGNED  	__________________, 2010

Company: _________________________________

}

}	Per:  ________________________________

}	Name:

}	Title:

}	I have authority to bind the corporation.