FCCP Non-Profit Housing Corporation

Bid Documents for

Caulking Repair of

Windows and Vents Perimeters

at

55 Glenn Hawthorne Blvd., Mississauga, Ontario

April 29, 2010

FCCP Non-Profit Housing Corporation

c/o Community First Developments Inc.

55 Glenn Hawthorne Blvd.

Mississauga, Ontario L5R 3S6

Telephone: 905-568-5292

Fax: 905-568-5293

1	General instructions

1.1	FCCP Non-Profit Housing Corp. (the "Non-Profit") located at 55 Glenn Hawthorne Blvd., Mississauga, Ontario is asking for Bids from experienced companies to provide caulking repair to the exterior joints along window, aluminum panel and vent perimeters.

1.2	It is expected that the project will be carried out in May or June 2010.

1.3	Your bid should include all permit costs, if any, to complete this project.

Quality Control

1.4	The Contractor shall be experienced in wall waterproofing and caulking repair, and be acceptable to the materials manufacturer.

Material Delivery, Storage & Handling

1.5	Deliver materials to job-site in new, dry, unopened, and well-marked containers showing product and manufacturer's name.  Deliver materials in sufficient quantity to allow continuity of work.

1.6	Store materials in dry area protected from weather condition.  Storage of materials inside the facility and/or at areas of the grounds is permitted only where designated and only with consent from the Management of FCCP Non-Profit Housing Corp.

1.7	Do not operate or situate material handling equipment in locations that will hinder smooth flow of vehicular or pedestrian traffic.  Debris shall not accumulate on the roof or on the ground around the job site.  Daily disposal and removal is required.

Site Condition

1.8	Contractor shall be responsible to police his men to ensure all areas where his men are working is kept clean, neat, and orderly.  At conclusion of job, an inspection will be done to satisfy the Management all areas of the building and grounds are in their original condition.

Environmental Requirements

1.9	Do not work in rain, or in presence of water.  Do not apply caulking materials if rain is imminent within 4 hours of application.

Safety Requirements

1.10	All application, material handling, and associated equipment shall conform to and be operated in conformance with WSIB and WHMIS safety requirements.  The Contractor's foreman shall have all applicable Material Data Safety Sheets on site and available for review at all times.  The Contractor must comply with City of Mississauga fire and safety requirements.  The Contractor must notify the Management whenever work is expected to be hazardous to the building residents and/or employees and/or operations.

Warranty

1.11	The Contractor shall provide a minimum 5-year labor and material warranty.  At the end of the project, the Contractor shall prepare and deliver to the Management a preventive maintenance plan for the work performed in this project.

Unit Prices

1.12	The Contractor shall provide unit prices for the following items:

a.	Caulking repair of window & vent perimeters	$/lf

b.	Glazing repair of windows				$/lf

Quantity Estimates

1.13	The estimated (unverified) quantities for the repairs are:

a.	Caulking repair of window & vent perimeters		10,000 lf

b.	Glazing repair of windows					2,500 lf

Allowances

1.14	This project has the following allowances:

a.	Unforeseen conditions		15% of the project cost

Important Dates

1.16	a.	Deadline for bid submission:		Thursday, May 13, 2010 at 3:00 p.m.

b.	Project commitment:			mid May 2010

c.	Project commencement (estimated)	late May 2010

d.	Project completion (estimated)	mid to late June 2010

2	Scope of work

Materials

2.1	The materials to be used are:

a.	Joints – Spectrum 3 by Tremco (colored to match existing)

b.	Glazing – Spectrum 2 by Tremco (colored to match existing)

c.	Primer – silicone porous surface primer by Tremco

Application Instructions

  - Window/aluminmum panel/vent joints:

- Remove all existing deteriorated caulking & sealant from window/aluminum panel/vent hand and/or power tools.

- Wipe the surface clean with Tremco #200 Cleaner.

- Apply a thin coating of Tremco Primer #6 to the metal surface and allow to dry tack free.

- Prime stucco side with Tremco silicone porous surface primer.

- Apply new Tremco sealant in a continuous bead, and tool to a smooth bump free and watertight surface.

  - Glass to metal glazing:

- Remove all existing deteriorated sealant and non-bonded particles from window to metal joints with hand and/or power tools.

- Wipe the surface clean with solvent such as xylol.

- Apply new Tremco sealant in a continuous bead, and tool to a smooth bump free and watertight surface.

BID FORM

To:	FCCP Non-Profit Housing Corporation

From:		Name and address of Bidder:

Job Site:	55 Glenn Hawthorne Blvd, Mississauga

The undersigned Bidder, having carefully examined the Bidding and Contract Requirements, Conditions of the Contract, Drawings, Specifications, dated April 29, 2010, and all subsequent Addenda, all as issued by the Owner, having visited the site, and being familiar with all conditions and requirements of the Work, hereby agrees to furnish all material, labor, equipment and services as described in the above documents, without exception, including all scheduled Allowances if any, necessary to complete the construction of:

The Contract for the above-named Project, in accordance with the requirements of the Bidding Documents, for the sum of:

Unit Prices:

a.	Caulking repair of window, panel & vent perimeters	$__________ / lf

b.	Glazing repair of windows					$__________ / lf

c.	Swing stage mobilization (if the cost is over and above of the same cost already included in the french balcony railing project)

$__________

Time of Completion

The undersigned Bidder proposes and agrees hereby to commence the Work of the Contract Documents on a date specified in a written Notice to Proceed to be issued by the Owner and shall fully complete the Work within the Contract Time indicated in the Supplementary Conditions.

Acknowledgement of Addenda

The undersigned Bidder acknowledges receipt of and use of the following Addenda in the preparation of this Bid:

Addendum No. 1, dated _____________

The undersigned further states that he/she is a duly licensed Contractor in the Province of Ontario, and that all fees, permits, insurance, WSIB, etc., pursuant to the submission of this proposal have been paid in full.

SIGNED  	__________________, 2009

Company: _________________________________

}

}	Per:  ________________________________

}	Name:

}	Title:

}	I have authority to bind the corporation.