Maintenance Specification

- Contract Term

- The servicing of the two (2) elevators in accordance with the Specification will commence on November 16th, 2009 and will continue until for a period of five (5) years until November 15th of 2014.

- The Contract will automatically terminate November 15th of 2014 unless a request for an extension of the term is submitted to the Contractor by the Owner and accepted by the Contractor.

- Contractor shall at least once per month examine, clean, adjust and lubricate all electrical and mechanical component of the elevators.

- Contractor shall provide the minimum monthly labour of five (5) hours combined for both elevators for the purpose of performing preventive maintenance procedures.

- Callback service

  - For great certainty, the Contractor acknowledges and agrees that the costs of regular and emergency callback services are included under the costs of the Contract as submitted on the quotation.

  - Contractor shall provide regular callback services 24 hours a day, every day of the year.

  - Contractor shall provide no charge emergency callback services 24 hours a day, every day of the year.

  - Emergency Callback service shall be provided within 45 minutes during regular working hours, and within 45 minutes during weekends and holidays, traffic and weather conditions permitting.

  - Emergency callback service in response to passenger entrapment shall be a maximum of 30 minutes.

  - An emergency situation shall be considered a passenger entrapment, any unsafe condition, report of fire or flood, or anytime that one of the elevators is out of service.  The service elevator being out of service is also considered an emergency situation.

  - Elevator telephones to be monitored by the Contractor 24 hours a day, every day of a year, at no additional cost.

- Exclusions

  - The Contractor shall not be responsible under the Contract to repair or maintain

    - Damage resulting from misuse of equipment or vandalism

    - Elevator cap enclosure including ceiling lights, hand rails (except to maintain tightness), floor coverings and telephone handsets.

    - Hoistway entrance frames

    - Door sills

    - Machine room heating and ventilation

    - Main disconnect switches

    - Components related to the building structure that form part of the elevator installation

  - If the repair or replacement of the components under subsection C(i) is required the contractor shall notify the Owner and submit to the owner a quotation to complete such work

- Termination

  - The Owner may terminate the Contract if the Contractor fails to obtain and maintain insurance as required.  If the Contractor fails to remedy such breach within five (5) business days after notice by the Owner, the Contractor will be liable for any and all costs, liabilities, damages, and penalties resulting to the Owner from such termination, unless a written waiver of the specific insurance requirements is provided to the Contractor by the Owner.

  - The Owner may terminate the Contract at any time prior to term of the Contract upon providing thirty (30) days written notice, for any of the following reasons:

    - if there is a significant change in the circumstances of the Contract as determined by the Owner, including but not limited to, an ownership change in regards to the elevators or the Contractor, or a major equipment modernization project;

    - If maintenance is not executed in strict accordance with this specification according to a report of any qualified independent third party and deficiencies in such report are not rectified in the time allotted by the said report;

    - If deficiencies that are the contractor’s responsibilities as listed in a Technical Standard and Safety Authority (T.S.S.A.) report are not completed in the time allotted in the T.S.S.A. report.  As a minimum, the contractor will assume responsibility for payment of any T.S.S.A. follow-up inspections that are required due to the contractor not fulfilling its duties as per the CAN/CSA B-44 Code requirements; and

    - If the contractor fails to remedy any grievance, with respect to the performance of the Contract that would not be subject to a report under D(iib) and D(iic), to the satisfaction of the Owner within the thirty (30) days following the Owner’s written notice of such grievance.

- Housekeeping

  - The Contractor shall maintain the machinery in clean condition, and keep the machine room, hoistway and pit area free from accumulation of dirt and debris.

  - All lubricants and used wipers are to be removed by the Contractor from the machine room.

  - The Contractor shall paint the machine room floor annually.

- Coverage

  - The Contractor shall maintain, repair or replace all elevator equipment including but not limited to:

- Machines , motors, bearings, sheaves, worms and gears, governors, controllers, selectors, signal devices, brakes, safety devices, door equipment, door operators, hoistway equipment, hoist ropes, governor ropes, traveling cables, compensating chains, emergency cab lighting and communications systems, exhaust fan and pit lights.

- Performance

  - The contractor shall maintain and adjust the elevator equipment to provide for:

    - Original contract speed, operating times, brake-to-brake times, door open times, door close times and dwell times.

    - A smooth ride with no harsh movements during acceleration, deceleration, leveling or stopping.

    - Smooth and quiet door operation.

    - Consistent leveling at all floors regardless of the load.

    - Dispatching in accordance with the manufacturer’s specification.

- Repair

  - All scheduled repairs are to be coordinated by the Contractor with building management two (2) weeks in advance.

  - In the event that a repair cannot be completed during an emergency callback situation, the Contractor shall commence the repair the morning of the following business day with immediate notice provided to building management.

- Inspections

In addition to the minimum maintenance requirements of the CAN/CSA B44 Code, the following checks are to be completed by the contractor according to the schedule listed below and, where required, the contractor shall take immediate corrective action for remedial work to repair, replace or re-adjust any component found to be worn, defective or out of adjustment:

  - Monthly

- Check elevator ride quality including acceleration, deceleration, speed, leveling and noises

- Check elevator machine room including cleanliness, temperature and ventilation

- Check controller

- Check operation of o the machine and brake

- Check hoist motor

- Check governor and tension sheave

- Check operation and the door operator and protective devices

- Check hall and door gibs, pick-up rollers, door locks and door closers

- Check roller guides and guide rail lubrication where applicable

- Check all position indicators, signal devices and call buttons

- Check all emergency communication devices

- Check cab ventilation fan

- Check entire hositway including pit

  - Quarterly

- Check the machine gear

- Check hoist rope traction sheave

- Check governor and operate manually

- Check buffer

- Check all hoistway switches

- Check emergency lighting in the elevator cab

  - Semi-Annual

- Check fire service operation

- Check emergency power operation

- Check controller voltages

- Check hoist ropes and traveling cables

- Check safeties

  - Annually

- Check all safety devices (mechanical and electrical)

- Check overload operation

- With respect to fire alarm testing, assist as required with the inspection of all hoistway fire alarms/detectors.  If required, it may be necessary to provide access for the alarm company to complete the inspections after regular working hours as per the requirements of the Owner.

- Annual Price Adjustment

  - Subject to J (ii), on the annual anniversary date of the Contract, the monthly price may be increased or decreased by the Contractor in direct proportion to the change in the hourly labour rate (including fringe benefits) of the local elevator union.

  - Any annual price increase shall be limited to a maximum of three percent (3%).

- Invoicing

The contractor shall submit a maintenance service invoice at the beginning of the month for payment of work to be competed in that month.  Payment will be due 45 days from receipt of invoice.

End of Specification